## Slide 1: Synthesis Based Design Techniques for Ultra Low Voltage Energy Efficient SoCs
Yanqing Zhang
February 27th, 2012

## Slide 2: Motivation for Ultra Low Voltage Design
Power
Performance
Wireless Sensor Nodes
Portable Electronics
Desktop Applications
Servers and Data Centers
Notes: So why ultra low voltage design? Here we see the application space of circuits, from the high-end performance apps of servers and data centers, all the way down to wireless sensor nodes, which require utlra low levels of power and energy and low performance. Ultra Low voltage design is geared toward the lower performance range, in these two bubbles, of which are of interest to us today.

## Slide 3: Motivation for Ultra Low Voltage Design
Application Characteristics:
1. Device lifetime
2. Robust functionality
3. Relatively small form factor
4. Speed not a major concern
[1]
Notes: The applications behind these circuits are typically characterized by needs for long device lifetime and very robust functionality over that lifetime, rather than focusing on speed and performance.
Relatively small form factor is a requirement as well.
For example, a pace maker, it’s especially important to have a prolonged lifetime. 10 years surgery, if we can prolong that, less pain and more economical.
Must have robustness, if it messes up, the results are drastic.

## Slide 4: Motivation for Ultra Low Voltage Design
Trend has been to use voltage scaling…
BUT IT’S NOT THAT SIMPLE!
[2]
Almost 2 orders-of-magnitude increase in energy efficiency
[1]
Notes: To cope with the requirement of device longevity, energy efficiency is of the most importance. Energy efficiency is defined as using the least amount of energy possible under the condition that a certain throughput requirement has been met. For the apps we care about, the throughput requirement is exsceptionally low most of the time, so really often times the problem comes down to pressing the minimal energy point, or finding it. Voltage scaling is becoming more and more a common solution to achieve energy efficiency, where people scale, they have these designs at nominal VDD, they scale them down, sacrificing speed that they don’t need, for low energy.
As we can see here, these are results for a ring oscillator, where x axis is VDD and Y axis is energy per cycle—which means we are modeling a circuit using a ring oscillator, we can achieve almost 2 orderes of magnitude increase in energy efficiency.
However, scaling VDD doesn’t automatically make things work. This is because transsitor characteristics change when we scale to ULV—near-vt and sub-vt, as we’ll find out in the next slides. Also, the general architectural strategy associated with designing SoCs should change if our main task is improving energy efficiency. In turn, these changes may compromise the circuit’s robustness, or in fact we will find that there is even more energy efficiency to be achieved.

## Slide 5: Key Challenges: Increased Significance of Leakage
% Leakage Energy/Total Energy for a Critical Path
Notes: In sub-Vt, speed drops off exponentially. Prolonged periods mean prolonged time gates are just sitting there leaking. meaning slower performance brings increase in the significance of leakage. This will compromise energy efficient design if not taken care of and why I say there is more energy efficiency to be achieved. If not taken care of, we cannot prolong deivce lifetime. This is for critical path.

## Slide 6: Key Challenges: Sensitivity to Variability
Local Variation of Delay for 4 Stage Inverter Chain
Exponential dependence on Vth increases uncertainty in timing closure metrics. This decreases chip yield.
Notes: The next challenge is the heightened sensitivty to variability in ULV regions. Because the current, and thus metrics like gate delay are exponentially dependent on threshold voltage, and unfortunately threshold voltage typically is modeled by varying normally in face of process variations, delays exhibit a log-normal distribution. This is for MC sims results for delay of 4 stage inverter ch. Log-normal distribution. More skewed and spread out. Usually at nominal VDD, gaussian, which is more compact and symmetric. If I put these gates into a logic path in my design, I can’t be sure I meed setup or hold time.

## Slide 7: Key Challenges: Efficient Hardware Selection
COTS Based WSN
Fully functional TX and DSP,
But 20mW power consumption
 Short lifetime
Custom IC Based IC
No DSP. 3 day lifetime.
Lacks functionality
Lifetime still short
[3]
High Speed SoCs
Very powerful. Low power so it is not power hog.
Not for ULV domain
Conventionally, we consider SPEED as main factor for system. Our requirements are: system LONGEVITY and ROBUST FUNCIONTALITY. We can really improve SoCs in ULV domain if we change our strategy.
Notes: On the architectural side, conventionally we consider speed as the main factor. In high perf SoCs, they’re very powerful and low power enough not be the system power hog, but they adhere to this design philosophy, so they are not suitable for ULVs. There have been several attempts to remedy this, but they are lacking in one aspect or another

## Slide 8: Summary of Dissertation Goals
PROJECT 1 (completed)
Design architecture for a Body Area Sensor Node (BASN) SoC capable of battery-less operation.
PROJECT 2
Local variation robust standard cell library for sub-Vt
Synthesis flow reducing leakage energy
PROJECT 3
Hold time robust design methodology
PROJECT 4
Alternative approach to DVFS
Notes: So to address these challenges, I’m proposing several projects that deal with them, each in their own definitive scope.

## Slide 9: Outline
Motivation
Hardware Selection for Energy Efficient SoC (BASN chip)
  Motivation
  Hypothesis
  Approach
  Results
Library Design and Characterization at ULVs for Robust Timing Closure
Hold Time Analysis and Timing Closure Method for Sub-threshold
Latch Based Design for Single-VDD Alternative Approach to DVFS

## Slide 10: Project 1: Hardware Selection for Energy Efficient SoC (BASN chip)
Notes: my first project which id like to propar as a completed chapter is sigital hardware selection fir energy eficient socs. better known as the basnchip, which has been tapd out and published. its a really kool chip witha lotnof unique features , really one of its knd. most of which is that it performs flexible data acquisition and processing batteryless, or poered off of a teg thermal electric generator.

## Slide 11
Wireless body area sensor nodes (BASN) enable inexpensive continuous monitoring of patients
Battery replacement/charging for body-worn devices may not be feasible or desirable
Information
Assessment,
Treatment
Motivation
Notes: this chip is motivated by the trend for long term portable healthcare. like i said one of the unique features is its ability to be powereed batteryless and off of energy harvesting mechanisms.
11

## Slide 12: Motivation
MCU
COTS Based WSN
Fully functional TX and DSP,
But 20mW power consumption
 Short lifetime
Custom IC Based IC
No DSP. 3 day lifetime.
Lacks functionality
Lifetime still short
[3]
BASNs exemplify design space requiring energy efficiency to the extreme
State-of-the-art low power modules help…but not full solution
On-chip processing a MUST (TX duty cycle, node size), but ‘throwing on an MCU’ entails high power ~100µW
Judicial hardware selection needed
Notes: the area i focusedd on, which was the digital hardware selection, i think was important. this is because the state of witeless health right now is butdened by this dillema where we either have long lifetime devices but they do much in diagnosis just sending signals periodically or they r very powerfully built but cost too much power. state of the art liw pwer circuit certainly help but too often is the case people just throw an mcu on chip to di data processing, but this is still highly inefficient.

## Slide 13: Hypothesis
~60µW
We can achieve a battery-less (energy harvesting) BASN SoC capable of various bio-signal acquisition and flexible data processing with state-of-the-art low power circuit design and judicial hardware selection
Notes: so pir hypothesis is that we can achieve a batteryless soc basn node by using state of the art low power circuits and the strategic integration of dogital components.

## Slide 14: Approach
0 50 100 150 200
Delay (µs)
Measured Energy/Op (pJ)
Accelerators:
Programmable FIR
Heart rate (R-R) extraction
Atrial Fibrillation (AFib) detection
Band energy envelope detection
Direct memory access (DMA)
Packetizer
Energy Efficiency / Sample
110x
6800x
4000x
0
1
2
3
4
30 Tap FIR | MCU | 6.3 nJ
 | Accel | 57.6 pJ
Env. Detect | MCU | 3.6 nJ
 | Accel | 530 fJ
R-R Extract | MCU | 12 pJ
 | Accel | 3 fJ
Notes: we ended up with the strategy of both having an mcu for maximum flexibility but also we strategically chose thes asic accelerators, to perform the most common tasks on chil efficiently. these accelerators spans from the fir dma and oacketiEr which r common for any type of basn node , to target application specific accels like rr and afib detecion.

## Slide 15: Significance
Has lower power, lower minimum input supply voltage, and more complete system integration than all other reported wireless BASN SoCs
first wireless biosignal acquisition chip powered solely from thermoelectric harvested power
Notes: in the end we succeeded in affirming our hypothesis and our chip achieved being the first ever batteryless woreless sensor node. the digital hadware was one of the many key players in lowering power and increasing energy efficiency.

## Slide 16: Outline
Motivation
Hardware Selection for Energy Efficient SoC (BASN chip)
  Motivation
  Hypothesis
  Approach
  Results
Library Design and Characterization at ULVs for Robust Timing Closure
Hold Time Analysis and Timing Closure Method for Sub-threshold
Latch Based Design for Single-VDD Alternative Approach to DVFS

## Slide 17: Project 2: Library Design and Characterization at ULVs for Robust Timing Closure
Notes: my firet new project has to do with library design and. haracterization

## Slide 18
Motivation
Static CMOS NOR2
Static CMOS NOR2 FAILS SNM @ TT corner with local variation
Notes: First, why do we need a new standard cell library? First motivation is the issue of yield. The yield for standard cells has been presented in prior art to be that of the passing of SNM tests. As you can see here is the butterfly curve for a NAND2 anad a NOR2 gate bak to bak. To pass SNM we need the curves to intersect with each other, but they fail to do so with local variations.
18

## Slide 19
Standard cell library essential to synthesis, but scaling industry standard cells aren’t sufficient for sub-Vt—fail SNM with variation
Motivation
Problem:
Weak devices (PMOS) +
Stacked transistor variation
Notes: This is because weak devices, in our case PMOSses that are in stacks in sub-vt sometimes become so weak when they vary that their pullup current cannot beat, or becomes the same order of magnitude as the off leakage of the pulldown, and thus can’t give a well defined enough ‘1’ and thus fails SNM. So that it why we need a new library.
19

## Slide 20
Motivation
Logic Gate
Logic Gate
Logic Gate
Logic Gate
Logic Gate
Logic Gate
LEAKING WITHOUT PURPOSE!
[4]
Notes: We know for a fact that people have turned all sorts of knobs, one of them being increasing gate length, to sacrifice speed but optimize leakage on non-critical paths. Sacrificing is speed is ok, because these paths are non-critical.
20

## Slide 21
Conventional method of ‘process corner based timing closure’ un-suitable for sub-Vt
Doesn’t capture sensitivity to local variation
Motivation
Notes: However, this method may be dangerous when considering cell characteriZation, which is extractng delay information about logic gates and setuphold info for storage implements. normally we do this by simulating these components at a fixed process corner and the delay extracted at those corners r supposedly valid for how our gates will act. this is largely untrue at ulvs because of heightened senstivity to variation. here we see simulation kf strings of inverter chains and we see how great their variation is. if i plotted delay and not log delay these curves would be quite spread out that u wouldnt be able to see all of it. clearly process corner characterization, which opnly provides one point of characterization, doesn’t capture this. So without being aware of local variation, we may slow the non-critical paths too much so that they become critical and failing setup.
21

## Slide 22
Hypothesis
1. Using TX-gate style logic, we can achieve lower energy consumption for a given yield when compared to static CMOS gates.
2. We can achieve decreased total energy with a flow that optimizes leakage on non-critical paths, but still ensures path yield with variation aware cell characterization.
Notes: whaT I’LL be doing is countering SNM failures in ultra low voltages with tx-gate style logic, and performing leakage optimization that is local variation aware for ensuring timing closure
22

## Slide 23
Proposed Approach
Notes: his flow chart shows the approach i propse to take. first i build the tx based library expand it with long length and optimized revister cells. then i do synthesis and write a script that replaces cells with their long length version to optimize leakage where suitable and do a lot of retiming. and the synthesis delay info will use the proposed library characterizaton mehid.
23

## Slide 24
Anticipated Contributions
Minimizing leakage in TX-based cells
Matching speed with static CMOS counterparts
Layout compactness issues
Anticipated Bottlenecks
Variation immune TX-Gate standard cell library (publication)
Variation aware path leakage optimization technique (publication)
Notes: 24

## Slide 25: Outline
Motivation
Hardware Selection for Energy Efficient SoC (BASN chip)
  Motivation
  Hypothesis
  Approach
  Results
Library Design and Characterization at ULVs for Robust Timing Closure
Hold Time Analysis and Timing Closure Method for Sub-threshold
Latch Based Design for Single-VDD Alternative Approach to DVFS

## Slide 26: Project 3: Hold Time Analysis and Timing Closure Method for Sub-threshold
Notes: my third project deals with robust hold time uirld in subt

## Slide 27
Motivation
tSKEW
Clock
Clock+skew
Data 1
Data 2
Clock
Clock +skew
Data 1
Data 2
Skew is increased in sub-Vt because of increased PVT variation sensitivity
Notes: as we know there r many factors that an lead to hld time failires like skew

## Slide 28
Motivation
Clock w/ BAD slew
Data 1
Data 2
Clock w/ BAD slew
Data 1
Data 2
Slew is decreased in sub-Vt because of increased PVT variation sensitivity
Notes: bad slew

## Slide 29
Motivation
Clock
Clock
Data 1
Data 2
Hold time, clock-q uncertainty in sub-Vt because of increased PVT variation sensitivity
Data 1
Data 2
Notes: and hld ribustness margin of the registers themselves measured in terms of holt time and clock to q delay.

## Slide 30
Motivation
tSKEW
Conventional method to solve hold time:
Use clock tree synthesis to design a tree with many levels (control skew) and large buffers(control slew)
Use buffer insertion to take care of hold time, clock-q
THIS WON’T WORK IN Sub-Vt!
Notes: onventional wisdom tells us the flow to ensure hold timong closure is to .../ and ...
but this wont work in subt be uase of pvt variations that make the transistors behave. differently

## Slide 31
Motivation
More levels=more skew! Contrary to conventional widsom…
Notes: or example, on the issue of skew, this plot teells us that leess clock levels rather thab more will br more robustt in subvt. these r monte carl simulations of a 138 state shift revisters where there r no hld buffers , slew os ideal and the only thing. hanged is the level of clock tree. because of increased senstivity to variations the more levels of buffers in the. lock tree the more skewness leading to less yield. so this goes. ontrary to. on rntional eisdom

## Slide 32
Motivation
Buffer insertion energy costly!
And still doesn’t solve our problem (subject to variation too…)
Notes: ext, the buffer insertionmethod to ensure there isenough delay on a logic path to fix hold errors has problrms too. here is a 128 shift revister with ideal slew and ideal skew and the obly thing chnaged is the amount if buffers i pu t jt. because the buffer delays themselves r subject to variation there is no assurance that they will solve the problem, even if we put 3 or 4 per oath. whats more, their energy consumption can cause the circuit consumption to be three times their normal ujbuffered value.

## Slide 33
Hypothesis
1. We can achieve a similar parameter controlling method suitable for sub-Vt by re-analyzing the effects of each parameter.
2. We can achieve a more energy efficient method for a given yield constraint using a novel two-phase clock based timing scheme
Notes: o its clear we have a problem because the standard flow wont work as it is. so i propose that we reanalye how sensitive hold failures r to each of the mechanisms of failing and come up with a new methodology for controlling those variables like skew and slew. for example if less levels of clock is better well do that. in addition becuase we see the shortcomings of burfer insertion for bold fix , we propose a novel hold fixing timing scheme using teo phase clock that rids he need for buffers. well talkk anout it in setail in the next slides.

## Slide 34
Approach
Notes: this diagram summarizes the approach ill take. First ill permutate these numbered variables, and run sims controlling the hold critical circuit so only one variable determines the hold yield and determine how we should design the circuit to maximize hold yield with tespect to each variable. bu then we would have a modified eda tool flow suitable fir subvt and it would give us thue lowes energy implementation for a given hold constraint. he next step is to compare the energ efficiency of this eda method wih the proposed two phase clock solution. and see which is better.

## Slide 35
Approach
Notes: the two phase clock method works like this. Because we anticipate skew and hold buffer insertion to be two key factors of the hold yield, were trying to seek out a method that minimies the impaxct of variaiton on thse variables. so first, insplit one reg into two pos edge latches and ask a dll to split the clock into teo phases. why doni do this? the scheme works like: with this well defined pulse which comes a delay later than the master clock edge the data gets trapped in between latches instead of racing to the next reg which. ould be still transparent because of clock skew. the data is released from the first reg or 2nd half latch after this delay at th edge of th pulse and is setup st the next register st the nextclock cycoe which is coorect. because i am aniticpating this dela and pulse length is erll sefined via a well designed low power dll incan now be tolerable of clock skew and nkt worry about buffer insertion variatoj.

## Slide 36
Anticipated Contributions
Simulation time for coming up with design methodology
DLL design for two-phase clocking
Incorporating timing scheme into synthesis flow
Anticipated Bottlenecks
Design methodology using EDA tools suitable for sub-Vt (publication)
A novel hold time fixing scheme using two-phase clocking (publication)
Notes: 36

## Slide 37: Outline
Motivation
Hardware Selection for Energy Efficient SoC (BASN chip)
  Motivation
  Hypothesis
  Approach
  Results
Library Design and Characterization at ULVs for Robust Timing Closure
Hold Time Analysis and Timing Closure Method for Sub-threshold
Latch Based Design for Single-VDD Alternative Approach to DVFS

## Slide 38: Project 4: Latch Based Design for Single-VDD Alternative Approach to DVFS
Notes: ok last project is about single vdd alternative to dvfs using dynamically pielined latches

## Slide 39
Motivation
Recent research has demonstrated near ideal energy savings using this concept by using three voltage islands.
[5]
Notes: so, dvfs has been growing in popularity as a solutioj to trade off performance and energy for dynamic workilowds. some approaches to it nclide multi vdd where circuits are conected to a certain vdd island depending oj the workload or state of the art resumts shiw u can get near ideal savings when u use three voltage islands with dithering.

## Slide 40
Motivation
Potential drawback: when considering total energy through DC-DC converter, may compromise energy savings
Notes: however the potential drawbak is the need for dc dc converters in delivering these voltage islands. the potential overhead fo dc dc converters in terms of energy and area is great. u either need a variable iutput converter which efficiency will not be optimized for diff voltage poiints leading to greater energy than expexted or multiple converters that take up area and still might not deliver power efficiently because of challenges involved at subvt. as an example, ive taken the previous plot and divided the energy points by 0.7 the highest efficiency for a converter operating in ilv to date to rstimate the fleffects of dc coverter efficiency. as u can see in mvdd it costs more and the pd s approach. ome off the ideal curve.

## Slide 41
Hypothesis
1. We can achieve better energy efficiency in DVFS by dynamically switching level of pipelining in a latch based design running off of single VDD for a certain frequency range.
Notes: therefore, my hypothesis is that we mght nor want diff ved domains. how do we do dvfs then? i propose an alternstive approach to dvfs using a lach based desifn tha operating on single vdd and scalig freq by dynamically switching the level of pipeling n te circuit. And that it’ll work for a certain range of frequency.

## Slide 42
Approach
Notes: my approach is becore i just start wroting. erilog building my deaign its worthwhile to construct a model of how my scheme might work. and it goes like this . inhave a dataflow path, modeled by an inverter chain,and insweep the hrouput. and i need to answer the question hiw much pipeline is needed to meet that throuput? and i also need to sweep vdd and ask myself, at what vdd and pipeline combinatioj is this most energy eficient? and thats hiw i know if this wild idea is even wirth it

## Slide 43
Approach
Notes: the end effect is that iw ill be aboe to. ompare these two schemes and evaluate if this idea does a ood kob afer i design the desied circuit according to conclusijs. of my model.

## Slide 44
Anticipated Contributions
Minimizing the overhead for switching the amount of pipelining
Latch-based timing issues
Anticipated Bottlenecks
Analysis of optimal latch pipelining for ULVs (publication)
Dynamic pipelining alternative approach to DVFS (publication)
Notes: 44

## Slide 45
Publications
1. Fan Zhang, Yanqing Zhang et al., “A Batteryless 19µW MICS/ISM-Band Energy Harvesting Body Area Sensor Node SoC”, to appear in 2012 International Solid-State Circuits Conference, 02/2012.
2. Benton H. Calhoun et al., “Body Sensor Networks: A Holistic Approach from Silicon to Users”, IEEE Proceedings
3. Yanqing Zhang and Benton H. Calhoun, “The Cost of Fixing Hold Time Violations in Sub-threshold Circuits”, 2011 Subthreshold Microelectronics Conference, 09/2011
4. Yanqing Zhang et. al., “Energy Efficient Design for Body Sensor Nodes”, Journal of Low Power Electronics and Applications, 04/2011.
5. Benton H. Calhoun, Sudhanshu Khanna, Yanqing Zhang, Joseph Ryan, and Brian Otis, “System Design Principles Combining Sub-threshold Circuits and Architectures with Energy Scavenging Mechanisms”, International Symposium on Circuits and Systems (ISCAS), Paris, France, pp. 269-272, 05/2010.
Notes: 45

## Slide 46
References
[1] A. Barth, “TEMPO 3.1: A Body Area Sensor Network Platform for Continuous Movement Assessment”, BSN 2009.
[2] B. Calhoun and A. Chandrakasan, “Characterizing and Modeling Minimum Energy Operation for Subthreshold Circuits”, ISLPED 2004
[3] S. Rai, et. al., “A 500uW Neural Tag with 2uVrms AFE and Frequency-Multiplying MICS/ISM FSK Transmitter”, ISSCC 2009
[4] H. L. Yeager, et. al. “Microprocessor Power Optimization through Multi-Performance Device Insertion”, VLSI 2004
[5]Y. Shakhsheer et. al. “A 90nm Data Flow Processor Demonstrating Fine Grained DVS for Energy Efficient Operation from 0.25V to 1.2V”, CICC 2011
Notes: 46

## Slide 47
Schedule: Key Anticipated Milestones
Project | Milestone (Publication for…) | Expected Date
BASN chip | Hardware platform comparison | Completed
BASN chip | Batteryless SoC chip | Completed
Library Design | TX-gate based standard cells | 09/2012
Library Design | Variation aware leakage optimization | 12/2012
Hold Closure | Sub-Vt hold time method using EDA tools | 12/2012
Latch DVFS | Latch pipelining analysis in sub-Vt | 01/2013
Latch DVFS | Alternative DVFS approach | 09/2013
Hold Closure | Two-phase clock method | 10/2013
Notes: A little about my schedule. In retrospect I would say that the detail I put in my proposal document may have been a bit overwhelming. I think I might have proposed 3 tapeouts…which means I’ll never finish. But I do want to work on these several proejcts, and in fact I think I won’t have that many tapeouts…some of them can be combined or some will be small ones…but what I think I really wanted to come across is my schedule of when I can be ready to publish, and I think u know, even 1 publication per project is enough to say I made a significant contribution. But we can definitely talk about it.
47

## Slide 48
THANK YOU!
“PhD Degrees:
You have to be Lin it to Lin it”
-Yanqing Zhang
Notes: 48

## Slide 49: How Does Synthesis Relate?
2. HDL Description
Module SoC_components (in, out, clk)
…
1. Determine Architecture
MCU?
Memories?
Accelerators?
Bus protocol?
3. Standard Cell Design
4. Characterization
INV:
delay=…
POWER=…
Leakage=…
5. Gate Translation
6. Timing Closure
Clock
Data
7. Place and Route
8. Chip Verification
DUT
Notes: These steps are affected by the changed transistor characteristics. If we don’t address them, any one of these steps can compromise deployment of a commercial product. WE cant improve then. Highlighted some of the major areas affected. So what I’m trying to do, my projects focusing on addressing coping with the drawbacks from scaling. For a fully deployable design.

## Slide 50: Key Challenges: Weakened Drive Strength
[2]
We would like a slower drop-off in frequency, because this leads to drastic increase in leakage
Ring Oscillator Frequency
Notes: The way I’m going to explain the problem, I’ll first explain the problem on a low level, and explain how they relate on a higher level of abstraction, how these things affect steps in the synthesis flow.
This is for ring oscillator. Drops of exponentially. Not good. If more gradual would be great.

## Slide 51: Key Challenges: Unbalanced FET Strengths
Standard cells are designed at nominal VDD . We can’t just scale VDD and expect balance. This constrains speed and increases leakage
Relative Strength of NMOS/PMOS
Notes: Speed constrained further obecause of imbalance. Sometimes pmos sometimes nmos. Minimam area=minimum energy, but LEAKAGE another problem. Increase area, but more active energy. Lose-lose situation.

## Slide 52: Approach
 | Energy per Instruction | Energy per Sample | Delay per Sample | Max achievable data rate | GOPS / W
GPP | 2.62 pJ | 210 pJ | 8 us (80 cycles) | 125 kHz | 4.76
FPGA | N/A | 2.22 pJ | 94.5 ns (1 cycle) | 10 MHz | 450
ASIC | N/A | 0.23pJ | 6.18 ns (1 cycle) | 150 MHz | 4348
Implemented same R-R extraction algorithm
Same technology, manual optimization of codes
100X energy efficiency for ASICs vs. GPPs
Use GPPs sparingly, steer processing to ASICs

## Slide 53: Approach
ADC
DMA/SRAM
Bio-signal Accelerators
Packetizer
Power and
Channel control
Sampling rate control
Power/clock gate, clock rate, and
bus control
Duty cycle, data rate control
Digitized VBOOST
DPM
Chip program
LNA
VBOOST
VGA
IMEM
MCU
Notes: As the energy efficient chip controller, the DPM issues custom instructions to control power-gating and channel select in the AFE, ADC sampling rate, sampled read of the digitized Vboost for power management.
DPM also controls the power/clock-gating of all the digital components, data flow in the bus, as well as the transmit duty-cycle and data rate.
-----------------
Here we show the specific control capabilities of the DPM. The DPM is a custom-ISA, energy efficient chip controller. Thus, the DPM has custom instructions that control the power gating of amps in the AFE and ADC channel muxing. It also controls the sampling rate of the ADC, and decides when it wants to read the Vboost value to check and see if the ‘stoplight’ color needs to change.
The DPM completely controls the data flow once the data is acquired in the AFE. Here we see that it controls the power and clock gating of all the digital components, and is able to steer the data to the right digital block by controlling the bus as well.
In the final stage of the signal path, the DPM also controls the Duty cycle and tx data rate for the transmitter, as well as when to turn on and off the XTAL and TX.

## Slide 54: Approach
Data processing
Data transmission
Data processing: max flexibility (generic path) or max efficiency (biosignal accelerators)
Data transmission: supports modes from streaming (100% DC) to rare event detection (~0% DC)
MCU: microcontroller
Notes: In the flexible signal path, the DPM controls reprogrammable data processing and transmission to suit the needs for different algorithms and applications
For the digital data processing, we have a generic path that maximizes flexibility. The microcontroller, or MCU, runs an arbitrary program from the SRAM IMEM and functions as a processing unit.
We’ve also integrated several custom bio-signal accelerators to maximize energy efficiency when performing frequently used functions such as FIR filtering, RR/Afib detection and Env. Detection.
Lastly, a mixed topology combining the MCU and custom accelerators can be used.
For data transmission, we can either stream at 100% DC, or selectively transmit on a timer or event base, which lower the duty cycle and the average power of the TX.

## Slide 55: Results
Time (s)
0 1 93 95 97 99 101 103 105 107
1
…
…
…
AFib begins
Chip detects AFib
0.8
0.6
0.4
0.2
0
0.5
0
When a rare AFib occurs, TX is enabled to transmit the last 8 beats of ECG (in the data memory).
19 µW total chip
Input ECG Signal (V)
AFib Detect (V)
Notes: Lastly, we configured the chip to detect an Afib event, in which case, the transmitter is enabled to transmit the last 8 beats of ECG waveform that is buffered in the data memory.
In this mode, the chip also consumes 19uW and can be powered from a 30mV input.
----------------------------
ECG is sampled at 256 sps. 2kB is allocated for ECG (2048/256=8 s)

## Slide 56: Results
ADC IN
(V)
TX EN
TX DATA
Time (s)
Every 5s, VBOOST is sampled to check for sufficient energy
DPM enables RF crystal oscillator (20ms) and TX (650µs)
19 µW total chip
Notes: Next, the chip extracts the R-R interval and transmit measured heart rate.
Once every 5s, Vboost is first sampled to check for sufficient energy, in which case the crystal osc is enabled for 20ms before TX transmission.
Here shows the detailed transmission of a 24-bit packet, including header, data and CRC.
In this mode, the chip consumes 19uW, and can be powered from a 30 mV input.
(Should we show “30mV input” in the slide?)

## Slide 57
Standard cell library essential to synthesis, but scaling industry standard cells aren’t sufficient for sub-Vt—fail SNM with variation
Motivation
Notes: Wireless body area sensor networks (BASN) help reduce healthcare cost and enable patients to freely move around during health monitoring. Biophysiological data (i.e. ECG, EMG, blood pressure, etc.) are first measured with on-body sensors. The data is conditioned, digitized on sensing tags and wirelessly transmitted to a base station for further processing. Assessment and treatment information is then fed back to the patients. Battery replacement for the wireless BASN tags may not be feasible or desirable. Therefore, there is a dire need to reduce the power consumption and form factor of these on-body tags
57

## Slide 58
Make the cells bigger?
Won’t work, greater active energy, not an insurance to robustness
Even if it did work, area at least quadruples
Motivation
Notes: 58

## Slide 59
Preliminary Results
Increased SNM @ FS corner
Static CMOS NOR2
TX-Gate NOR2
Notes: 59

## Slide 60
Preliminary Results
Increased SNM @ SS corner
Static CMOS NOR2
TX-Gate NOR2
Notes: 60

## Slide 61
Preliminary Results
TX-Gate NOR2
TX-Gate NOR2 PASSES SNM @ TT corner with local variation
Notes: 61

## Slide 62
Preliminary Results
Hold time is quite immune to slew variation
Slew affects clock-q—there is a limit to slew before clock-q becomes detrimental

## Slide 63
Preliminary Results
Low power DLL makes novel two-phase timing scheme possibly worthy
 | P2p jitter | Frequency | Power | % Jitter/Freq | Main Contribution
DLL | 373 ps | 100 MHz | 15 uW | 3.73% | Low Power
Header/Footer Array
CLK_IN
Current Starved Inverters
Weak Latches
Level Restorers
Out_b
Out

## Slide 64
Motivation
DVFS provides the ability to trade-off energy and delay to cater to variable workloads
[4]

## Slide 65
Approach

## Slide 66
Preliminary Results
Efficiency of latches have the potential to mitigate the pipelining overhead of this scheme

## Slide 67
Preliminary Results
Efficiency of latches have the potential to mitigate the pipelining overhead of this scheme